## Slide 1: “Raspberry Jam” Monitoring your world

## Slide 2: What is the problem?
Existing home security and environment monitoring systems are expensive and often times bulky.
Our goal is to design a working prototype that is cheaper and has more configurability than current solutions on the market
As an example, consider Nest. Nest sells HI definition cameras whose video feed can be viewed remotely using a smartphone. The cost for one of these cameras? $200…
We beleive our system can achieve the same functionality for a fraction of the cost, albeit at a lower video resolution
JAM

## Slide 3: Summary and Motivation of Project Goals
Create a working prototype capable of streaming video, motion sensing alerts, and other useful information to a web page accessible remotely by any device with a web browser
Our team’s motivation for this project was driven primarily by our desire to test and develop our skills in creating an embedded system that communicates over the web. Additionally, we sought to create a system that is more affordable than current market solutions.
One of the key features of our product resides in it’s configurability. We seek to create a product whose hardware can be easily customized, thereby enabling each user to add or remove specific features based upon there application
JAM

## Slide 4: Proposed Solution
Our design utilizes a Raspberry Pi Model B acting as an intermediary between our home monitoring system and a website hosted locally on the Pi. *Note- Use of the term “Pi” refers specifically to the Raspberry Pi Model B Microcomputer
Our monitoring system will include a camera, a motion detector, and an alarm system.
Our monitoring system will also be configurable, meaning additional hardware can be added or removed if the user wants more (or less) functionality from the system based upon their needs
Some current ideas for add-ons include temperature sensors and light sensing diodes capable of monitoring temperature and room brightness
JAM

## Slide 5: Specifications
The primary selling points of our product are its low cost relative to similar solutions on the market and its hardware configurability.
Our system will be capable of monitoring environmental conditions in a single 20x20 square foot room.
Multi-room monitoring is also a viable feature. This implantation would require a secondary PCB, and while we will not be implementing this feature in the prototype, we plan on providing the software framework to make this possible as a testament to the device’s configurability. In other words, adding a second monitoring system would be a “plug-and-play” feature.
JAM

## Slide 6: Technical Specifications/Performance
Feature | Specifications
Size and weight | 120 cubic inches; 3 lbs
Video Output | 480p continuous video stream
Power Consumption | 0.06 kWh per month if monitoring is active 80% of the time
Motion Sensor Range (Maximum room size) | 20 feet
Alarm | Store up to 5 custom alarm sounds at any time
Connectivity | Any device with an internet connection and HTML5 capable web browser
Hardware Add-ons | Temperature Sensor, Light sensor
Maximum number of rooms that can be monitored | 2
JAM

## Slide 7: Design Approach
Light Sensing Diode
Temperature Sensor
On Board PCB
JAM

## Slide 8: Design Approach cont.
Our design features a custom PCB on which all hardware components will either be mounted with screws or soldered on.
Just as the Pi acts as an intermediary for processed data between the PCB and the web server, the PCB acts as the intermediary for raw data between the monitoring components (video camera, motion sensor, and alarm system) and the Pi
JAM

## Slide 9: Design Control Flow
Raw data is acquired from the video camera, motion detector, and alarm system, temperature sensor, and light sensing diode
On board PCB circuit routes acquired to appropriate GPIO pin on the Pi. Some hardware components, such as the temperature sensor and light sensing diode output analog signal, these signals will be converted to digital using an ADC on the PCB. (The Pi does not have any analog input or output pins)
Using Python scripts running locally on the Pi, the raw data will be processed and interpreted into meaningful data.
This data will be sent over the network to an http web server hosted on the Pi.
The web page URL will be accessible by any device with a web browser
From the web page, commands can be sent to the Pi. These include shutting the monitoring system off, controlling alarm output sound and volume, and disarming the motion sensor.
JAM

## Slide 10: Manpower
Mike – JavaScript web application, network bidirectional communication (websocket)
John – PCB design (CAD), Python Scripting, hardware prototyping
Thadoe – PCB physical circuit design, Software debugging (Python and JavaScript), webserver
JAM

## Slide 11: Schedule
Chart: 
| Order Hardware | Milestone Report 1 | Layout Circuit Schematic | PCB Design | Build prototype circuit/test | Scripting for web application | Python scripting for hardware | Python scripting for web server | Design Review | Outfit PCB with hardware/test | Milestone Report 2 | Build Enclosure for System | Integrate system into enclosure | Debug all software | Milestone Report 3 | Integrate Possible hardware add-ons | Final Review
Start Date | 42401 | 42408 | 42408 | 42401 | 42415 | 42401 | 42409 | 42401 | 42422 | 42444 | 42430 | 42451 | 42452 | 42452 | 42458 | 42467 | 42479
Duration | 7 | 8 | 7 | 35 | 8 | 15 | 56 | 43 | 10 | 8 | 8 | 32 | 7 | 37 | 10 | 20 | 10
Mike
John
Thadoe
All
JAM

## Slide 12: Cost Estimate
Component | Price |  |  |  |  |  |  | 
Raspberry Pi Model B | $35.00 |  |  |  |  |  |  | 
ADC (MAX11645EUA+) (x2) | $2.70 |  | 10-bit | 2 channel | I2C | SAR |  | 
Rasp Pi On Board Cam | $16.41 |  |  |  |  |  |  | 
Speaker (x2) | $1.98 |  | 0.2W | About 80 dB | 8 Ohm | 30 mm Diameter |  | 
Temperature Sensor (x2) | $1.98 |  |  |  |  |  |  | 
Op Amp (x2) | $1.98 |  | 4 Channel | 3 MHz | 70 dB |  |  | 
Photodiode (x2) | $1.98 |  |  |  |  |  |  | 
Case Sheet Metal | $8.80 |  |  |  |  |  |  | 
Printed Circuit Board | $30.00 |  |  |  |  |  |  | 
Bulk Components | $10.00 |  |  |  |  |  |  | 
Relay(s) | $10.00 |  |  |  |  |  |  | 
Total Hardware Cost | $110.83 |  |  |  |  |  |  | 
Engineering Cost/Salary | $28,800 |  | Total manhours: 180 |  |  | Hourly Wage $80 | (100% overhead) | 
Total Development Cost | $28110.83 |  |  |  |  |  |  | 
JAM

## Slide 13: Meet our Team!
John Darling
Mike Ross
Thadoe Swan-Yi
JAM

## Slide 14: Mike Ross
JAM

## Slide 15: John Darling
Technical Experience/Skills
JAM

## Slide 16: Thadoe Swan-Yi
JAM